## Slide 1: Basic Network Devices
CompTIA Network+ Certification

## Slide 2: Objectives
Install and configure hubs, bridges, and switches
Describe the purposes and functions of Virtual LANs (VLAN)
Understand the use of spanning tree to prevent switching loops
Notes: The number in the bottom right corner of the slides refers back to the page where this topic starts in the course book.

## Slide 3: Hubs
Basis of shared Ethernet (physical star – logical bus)
Multiport repeater
  Regenerate and repeat an incoming transmission over all ports (except the source port)
  All ports in same collision domain

## Slide 4: Bridges
Legacy Ethernet devices used to segment networks and reduce contention
Operate at data link layer
Can also join segments using different media (e.g. coax to twisted-pair)

## Slide 5: Switches
Basis of switched Ethernet
Replaced hubs and bridges
Microsegmentation
  Switch establishes point-to-point links between nodes
  The collision domain is reduced to the link between a single node and the switch (i.e. NO collisions are possible if port is configured for full duplex)
MAC address table / Content Addressable Memory (CAM)
Wide range of devices for residential or Small Office Home Office (SOHO) up to enterprise use

## Slide 6: Managing Switches
Managed vs unmanaged
Management interface
  Console port / Command Line Interface (CLI)
  Management port (connect over IP network)
    Web interface using HTTP / HTTPS
    Virtual terminal over Telnet / SSH (CLI)
  Network management (SNMP [Simple Network Management Protocol])
In-band vs out-of-band
Management accounts
  Users / passwords configured on each device
  AAA (Authentication, Authorization, and Accounting) configuration for centralized account management and authorization

## Slide 7: Switch Interface Configuration
Speed and duplex mode
Autonegotiation – switch and adapter negotiate connection parameters (speed / duplex)
IP address assignment
Default gateway

## Slide 8: Virtual LANs (VLAN)
Create separate broadcast domains
VLAN assignment
  Static (port-based)
  Dynamic (assign by host MAC, IP, authentication, etc)
Traffic between VLANs must be routed
Create zones for security / administration

## Slide 9: Power over Ethernet (PoE)
Supplies electrical power to devices over Ethernet cable
Suitable for IP phones, wireless access points, thin clients, IP cameras, etc
802.3af – 13W
802.3at – 25W (PoE+)
Supplying device (e.g. switch) is Power Sourcing Equipment
  PoE switch is an end-span
  Power injector is a mid-span
  Mode A (phantom power) and Mode B

## Slide 10: Network Devices
Modems
Repeater
NIC
Wireless NIC
Access Point
Firewall

## Slide 11: Server Types
DHCP
DNS
DC
Exchange