## Slide 1: Internet Protocol

## Slide 2: Binary / Decimal Conversion
Number bases
  Place value
  Base 10 (Decimal)
  Base 2 (Binary)
Converting between binary and decimal

## Slide 3: Subnet Masks
IP address represents both a network ID and host ID
A mask is applied to identify the network and host portions
A “1” in the mask means corresponding bit in the address is part of the network ID
“1”s in mask must be contiguous
  11111111 11110000 00000000 00000000 – VALID
  11111111 00000000 11110000 00000000 - INVALID

## Slide 4: ipconfig / ifconfig

## Slide 5: IP Routing Basics
Default gateway
Routing decision
Route selection / route table
Fragmentation

## Slide 6: ICMP
Internet Control Message Protocol (ICMP)
Message types
  Destination unreachable
  Time exceeded
  Redirect

## Slide 7: ping
ping IPAddress | HostName
Reply from, round trip time and packet loss
  Detect whether a link is slow or experiences packet loss
  Use tracert to identify where on the route there is a problem
Destination unreachable
  No route to host
  Check IP configuration
  Check router (default gateway)
No reply / timed out
  Host / interface is down
  Host cannot route reply
  Firewall

## Slide 8: Interpreting ping Output
Ping the loopback address (ping 127.0.0.1)
Ping the host’s IP address
Ping the IP address of the default gateway
Ping the IP address of a remote host